PROGRAM TestQuad

  use timers
  type(TimerType) :: func1Time,func2Time,func3Time

  REAL*8 left, right, result, eps, Quad
  REAL*8 Func1, Func2, Func3
  EXTERNAL Func1, Func2, Func3

! Initialise timers
  call TimerCreate(func1Time,"Func1")
  call TimerCreate(func2Time,"Func2")
  call TimerCreate(func3Time,"Func3")

  call TimerOn(func1Time)
  left = 0.0
  right = 1.0
  eps = 1.0E-7
  result = Quad (Func1, left, right, eps)
  call TimerOff(func1Time)

  PRINT *, "Result for Func1 = ", result
  call TimerPrint(func1Time)

  call TimerOn(func2Time)
  left = 0.0
  right = 1.0
  eps = 1.0E-7
  result = Quad (Func2, left, right, eps)
  call TimerOff(func2Time)

  PRINT *, "Result for Func2 = ", result
  call TimerPrint(func2Time)

  call TimerOn(func3Time)
  left = 0.0
  right = 1.0
  eps = 1.0E-7
  result = Quad (Func3, left, right, eps)
  call TimerOff(func3Time)

  PRINT *, "Result for Func3 = ", result
  call TimerPrint(func3Time)

END PROGRAM TestQuad

REAL*8 FUNCTION Quad (Func, left, right, epsilon)
  REAL*8 left, right, epsilon, Func

! *** Adaptive Quadrture

  INTEGER STACKSIZE,IL,IR,IE
  PARAMETER (STACKSIZE = 100000,IL=1,IR=2,IE=3)

  REAL*8 stack (3,STACKSIZE)
  INTEGER stackpointer

  REAL*8 result, abserror, l, r, m, est1, est2, eps

  stackpointer = 1
  stack(il,stackpointer) = left
  stack(ir,stackpointer) = right
  stack(ie,stackpointer) = epsilon

  result = 0.0

  call Stackops(stackpointer,stack,result,Func)

  Quad = result

  RETURN
END FUNCTION Quad

SUBROUTINE Stackops(stackpointer,stack,result,Func)

  INTEGER STACKSIZE,IL,IR,IE
  PARAMETER (STACKSIZE = 100000,IL=1,IR=2,IE=3)

  REAL*8 stack(3,STACKSIZE)
  INTEGER stackpointer

  REAL*8 result, Func
  REAL*8 abserror, l, r, m, est1, est2, eps

  INTEGER active_threads, work

  active_threads = 0

!$OMP parallel default(none) &
!$OMP private(abserror, l, r, m, est1, est2, eps, work) &
!$OMP shared(stack, stackpointer, active_threads) &
!$OMP reduction(+: result)

  DO WHILE (stackpointer .GE. 1 .OR. active_threads .NE. 0)

! *** Pop next interval off stack.
!$OMP critical (pop)
     work = 0
     IF (stackpointer .GT. 0) THEN
        work = 1
        !$OMP ATOMIC
        active_threads = active_threads + 1
        l = stack(il,stackpointer)
        r = stack(ir,stackpointer)
        eps = stack(ie,stackpointer)
        stackpointer = stackpointer - 1
     END IF
!$OMP END critical (pop)

IF (work .EQ. 0) THEN
   cycle
END IF

! *** Compute estimates.

     m = 0.5 * (l + r)
     est1 = 0.5 * (r - l) * (Func(l) + Func(r))
     est2 = 0.5 * ((m - l) * (Func(l) + Func(m)) + &
        (r - m) * (Func(m) + Func(r)))
     abserror = ABS(est2-est1) / 3.0

! *** Check for desired accuracy: push both halves onto the
! *** stack if not accurate enough.

     IF (abserror .LE. eps) THEN
! *** ours

        result = result + est2
!$OMP ATOMIC
        active_threads = active_threads - 1
! *** ours
     ELSE
        IF (stackpointer+2 .GT. STACKSIZE) THEN
        PRINT *, "Stack too small, try STACKSIZE = ", 2*STACKSIZE
        STOP
        END IF

! *** ours
!$OMP critical (pop)
! *** ours
        stackpointer = stackpointer + 1
        stack(il,stackpointer) = l
        stack(ir,stackpointer) = m
        stack(ie,stackpointer) = eps * 0.5

        stackpointer = stackpointer + 1
        stack(il,stackpointer) = m
        stack(ir,stackpointer) = r
        stack(ie,stackpointer) = eps * 0.5
! *** ours
        !$OMP ATOMIC
        active_threads = active_threads - 1
!$OMP END critical (pop)
! *** ours

     END IF
  END DO
!$OMP end parallel
  RETURN
END SUBROUTINE Stackops

REAL*8 FUNCTION Func1 (x)

  REAL*8 x, q
  INTEGER n, i

  n = 2000
  q = 1000.0

  DO i=1,n
     q = q - x
  END DO
  if (q.eq.1.0d10) print *,q

  Func1 = x * x
  RETURN
END FUNCTION Func1

REAL*8 FUNCTION Func2(x)

  REAL*8 x, q
  INTEGER n, i

  n = 20000
  q = 1000.0

  DO i=1,n
     q = q - x
  END DO
  if (q.eq.1.0d10) print *,q

  Func2 = x * x
  RETURN
END FUNCTION Func2

REAL*8 FUNCTION Func3 (x)

  REAL*8 x, q
  INTEGER n, i

  n = 200000
  q = 1000.0

  DO i=1,n
     q = q - x
  END DO
  if (q.eq.1.0d10) print *,q

  Func3 = x * x
  RETURN
END FUNCTION Func3

Overhead sources by type.

Non-parallel code: The stack, stackpointer and active_threads variables are shared amongst all the cores. It is necessary in order to implement a correct parallel algorithm for the integral calculation and a termination algorithm. When a thread gets a task from the stack, it needs to modify the stackpointer variable. Then, when it finishes and evaluates that more work is needed to achieve better precision, it will modify the stack and the stackpointer variables again to insert two more tasks. Whenever a thread is working on this process, it increments the active_threads counter and when it finishes, it will decrement it. Since all threads will write to these variables, we need to protect them with contention mechanisms, which prevent a section of code from being executed by more than one thread at any one time. With parallelism gone, this code becomes sequential, thus producing this type of overhead.

Synchronisation: This corresponds to the critical sections in the code, along with the atomic instructions, which are used to handle contention of the stack and stackpointer variables and the active_threads counter (variables shared amongst all cores). The costs of the locking and unlocking mechanisms (used for the critical sections), the cost of checking if a variable is locked or unlocked, and the cost of the atomic directive procedures compose this overhead. According to the results of the experiments shown in this report, a higher number of threads increases this overhead. This overhead is also increased when the tasks performed are less complex. As the tasks become less complex, the time to execute each task decreases, however the time taken to perform the synchronisation processes remains constant regardless of task complexity. This means that a greater proportion of the total time of execution (including the synchronisation and executing the task) will be spent synchronising. In less complex tasks, modifications to the shared variables will occur more often and contention will increase.

Synchronization overhead
Number of Cores
Execution Time (s)

- Memory access:
- Scheduling (parallel control):